## Slide 1: Sequential Logic

## Slide 2: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:

## Slide 3: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:

## Slide 4: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state

## Slide 5: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state

## Slide 6: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state

## Slide 7: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state

## Slide 8: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state

## Slide 9: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory

## Slide 10: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory

## Slide 11: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory

## Slide 12: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory

## Slide 13: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory
Time

## Slide 14: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory
Low – Tick – 0
High – Tock – 1
Time

## Slide 15: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory
Low – Tick – 0
High – Tock – 1
Time

## Slide 16: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory
Time
Cycle
Low – Tick – 0
High – Tock – 1

## Slide 17: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory
Time
Cycle
Represented by binary siignal
circuitry simultaneously broadcasts to every sequential chip
Low – Tick – 0
High – Tock – 1

## Slide 18: Remembering
All previous chips have been combinational: depend only on combination of inputs important for eg. ALU, but…
Sequential chips: memory elements that preserve data over time store and recall values
Flip-flops = building blocks binary cells, registers, memory banks, counters
Remembering is inherently time-dependent: you remember now what has been committed to memory before requires a clock:
Cannot maintain state
Provide memory
Time
Cycle
Represented by binary siignal
circuitry simultaneously broadcasts to every sequential chip
Low – Tick – 0
High – Tock – 1

## Slide 19: DFF
In this book we use data flip-flops (DFF) and consider them primitive
: outputs previous input
Basis of binary cells, registers, RAM, etc.
All DFFs are connected to the same master clock “chorus”
Beginning of clock cycle: all the DFFs output previous input
Latched: changes in their inputs don’t immediately affect output
DFFs affected a billion times per second (computer´s clock frequency) simultaneaously (feeding master clock to all DFFs)

## Slide 20: DFF
In this book we use data flip-flops (DFF) and consider them primitive
: outputs previous input
Basis of binary cells, registers, RAM, etc.
All DFFs are connected to the same master clock “chorus”
Beginning of clock cycle: all the DFFs output previous input
Latched: changes in their inputs don’t immediately affect output
DFFs affected a billion times per second (computer´s clock frequency) simultaneaously (feeding master clock to all DFFs)

## Slide 21: DFF
In this book we use data flip-flops (DFF) and consider them primitive
: outputs previous input
Basis of binary cells, registers, RAM, etc.
All DFFs are connected to the same master clock “chorus”
Beginning of clock cycle: all the DFFs output previous input
Latched: changes in their inputs don’t immediately affect output
DFFs affected a billion times per second (computer´s clock frequency) simultaneaously (feeding master clock to all DFFs)

## Slide 22: DFF
clock input (chip depends on time)
In this book we use data flip-flops (DFF) and consider them primitive
: outputs previous input
Basis of binary cells, registers, RAM, etc.
All DFFs are connected to the same master clock “chorus”
Beginning of clock cycle: all the DFFs output previous input
Latched: changes in their inputs don’t immediately affect output
DFFs affected a billion times per second (computer´s clock frequency) simultaneaously (feeding master clock to all DFFs)

## Slide 23: DFF
In this book we use data flip-flops (DFF) and consider them primitive
: outputs previous input
Basis of binary cells, registers, RAM, etc.
All DFFs are connected to the same master clock “chorus”
Beginning of clock cycle: all the DFFs output previous input
Latched: changes in their inputs don’t immediately affect output
DFFs affected a billion times per second (computer´s clock frequency) simultaneaously (feeding master clock to all DFFs)
clock input (chip depends on time)

## Slide 24: DFF
In this book we use data flip-flops (DFF) and consider them primitive
: outputs previous input
Basis of binary cells, registers, RAM, etc.
All DFFs are connected to the same master clock “chorus”
Beginning of clock cycle: all the DFFs output previous input
Latched: changes in their inputs don’t immediately affect output
DFFs affected a billion times per second (computer´s clock frequency) simultaneaously (feeding master clock to all DFFs)
clock input (chip depends on time)

## Slide 25: DFF
In this book we use data flip-flops (DFF) and consider them primitive
: outputs previous input
Basis of binary cells, registers, RAM, etc.
All DFFs are connected to the same master clock “chorus”
Beginning of clock cycle: all the DFFs output previous input
Latched: changes in their inputs don’t immediately affect output
DFFs affected a billion times per second (computer´s clock frequency) simultaneaously (feeding master clock to all DFFs)
clock input (chip depends on time)

## Slide 26: DFF
In this book we use data flip-flops (DFF) and consider them primitive
: outputs previous input
Basis of binary cells, registers, RAM, etc.
All DFFs are connected to the same master clock “chorus”
Beginning of clock cycle: all the DFFs output previous input
Latched: changes in their inputs don’t immediately affect output
DFFs affected a billion times per second (computer´s clock frequency) simultaneaously (feeding master clock to all DFFs)
clock input (chip depends on time)

## Slide 27: DFF
In this book we use data flip-flops (DFF) and consider them primitive
: outputs previous input
Basis of binary cells, registers, RAM, etc.
All DFFs are connected to the same master clock “chorus”
Beginning of clock cycle: all the DFFs output previous input
Latched: changes in their inputs don’t immediately affect output
DFFs affected a billion times per second (computer´s clock frequency) simultaneaously (feeding master clock to all DFFs)
clock input (chip depends on time)

## Slide 28: Registers 1-bit register
Stores a value over time
Single-bit register / bit / binary cell: stores 0 or 1
: depends on load bit
load = 0 keep current value read
load = 1 load new value write
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits

## Slide 29: Registers 1-bit register
Stores a value over time
Single-bit register / bit / binary cell: stores 0 or 1
: depends on load bit
load = 0 keep current value read
load = 1 load new value write
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits

## Slide 30: Registers 1-bit register
Stores a value over time
Single-bit register / bit / binary cell: stores 0 or 1
depends on load bit
load = 0 keep current value read
load = 1 load new value write
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits

## Slide 31: Registers 1-bit register
Stores a value over time
Single-bit register / bit / binary cell: stores 0 or 1
depends on load bit
load = 0 keep current value read
load = 1 load new value write
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits

## Slide 32: Registers 1-bit register
Stores a value over time
Single-bit register / bit / binary cell: stores 0 or 1
depends on load bit
load = 0 keep current value read
load = 1 load new value write
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits

## Slide 33: Registers 1-bit register
Stores a value over time
Single-bit register / bit / binary cell: stores 0 or 1
depends on load bit
load = 0 keep current value read
load = 1 load new value write
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits
/**
* 1-bit register:
* If load[t] == 1 then out[t+1] = in[t]
* else out does not change (out[t+1] = out[t])
*/
CHIP Bit {
IN in, load;
OUT out;
PARTS:
Mux(a=dffout, b=in, sel=load, out=o2);
DFF(in=o2, out=dffout, out=out);
}

## Slide 34: Registers multi-bit register
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits

## Slide 35: Registers multi-bit register
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits

## Slide 36: Registers multi-bit register
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits
/**
* 16-bit register:
* If load[t] == 1 then out[t+1] = in[t]
* else out does not change
*/
CHIP Register {
IN in[16], load;
OUT out[16];
PARTS:
Bit(in=in[0], load=load, out=out[0]);
Bit(in=in[1], load=load, out=out[1]);
Bit(in=in[2], load=load, out=out[2]);
Bit(in=in[3], load=load, out=out[3]);
Bit(in=in[4], load=load, out=out[4]);
Bit(in=in[5], load=load, out=out[5]);
Bit(in=in[6], load=load, out=out[6]);
Bit(in=in[7], load=load, out=out[7]);
Bit(in=in[8], load=load, out=out[8]);
Bit(in=in[9], load=load, out=out[9]);
Bit(in=in[10], load=load, out=out[10]);
Bit(in=in[11], load=load, out=out[11]);
Bit(in=in[12], load=load, out=out[12]);
Bit(in=in[13], load=load, out=out[13]);
Bit(in=in[14], load=load, out=out[14]);
Bit(in=in[15], load=load, out=out[15]);
}

## Slide 37: Registers multi-bit register
Multiple 1-bit registers any width of register
“word” = 16, 32, or 64 bits
/**
* 16-bit register:
* If load[t] == 1 then out[t+1] = in[t]
* else out does not change
*/
CHIP Register {
IN in[16], load;
OUT out[16];
PARTS:
Bit(in=in[0], load=load, out=out[0]);
Bit(in=in[1], load=load, out=out[1]);
Bit(in=in[2], load=load, out=out[2]);
Bit(in=in[3], load=load, out=out[3]);
Bit(in=in[4], load=load, out=out[4]);
Bit(in=in[5], load=load, out=out[5]);
Bit(in=in[6], load=load, out=out[6]);
Bit(in=in[7], load=load, out=out[7]);
Bit(in=in[8], load=load, out=out[8]);
Bit(in=in[9], load=load, out=out[9]);
Bit(in=in[10], load=load, out=out[10]);
Bit(in=in[11], load=load, out=out[11]);
Bit(in=in[12], load=load, out=out[12]);
Bit(in=in[13], load=load, out=out[13]);
Bit(in=in[14], load=load, out=out[14]);
Bit(in=in[15], load=load, out=out[15]);
}

## Slide 38: RAM multi registers
Stack registers memory bank of any length
Random Access Memory
Directly access randomly chosen words irrespective of its physical location in equal speed
For n-register RAM
Stack n registers
Assign unique address (j = 0 – n-1)
Build gate logic to select register at address j
3 inputs: data input, address input, and load bit
load = 0 read: RAM outputs value of selected register
load = 1 write: commit input value to register RAM will start
emitting in next time unit
basic RAM design
width: width of their words eg. 32 or 64 bits
size: number of words eg. hundreds of millions

## Slide 39: RAM multi registers
Stack registers memory bank of any length
Random Access Memory
Directly access randomly chosen words irrespective of its physical location in equal speed
For n-register RAM
Stack n registers
Assign unique address (j = 0 – n-1)
Build gate logic to select register at address j
3 inputs: data input, address input, and load bit
load = 0 read: RAM outputs value of selected register
load = 1 write: commit input value to register RAM will start
emitting in next time unit
basic RAM design
width: width of their words eg. 32 or 64 bits
size: number of words eg. hundreds of millions

## Slide 40: RAM multi registers
Stack registers memory bank of any length
Random Access Memory
Directly access randomly chosen words irrespective of its physical location in equal speed
For n-register RAM
Stack n registers
Assign unique address (j = 0 – n-1)
Build gate logic to select register at address j
3 inputs: data input, address input, and load bit
load = 0 read: RAM outputs value of selected register
load = 1 write: commit input value to register RAM will start
emitting in next time unit
basic RAM design
width: width of their words eg. 32 or 64 bits
size: number of words eg. hundreds of millions

## Slide 41: RAM multi registers
Stack registers memory bank of any length
Random Access Memory
Directly access randomly chosen words irrespective of its physical location in equal speed
For n-register RAM
Stack n registers
Assign unique address (j = 0 – n-1)
Build gate logic to select register at address j
3 inputs: data input, address input, and load bit
load = 0 read: RAM outputs value of selected register
load = 1 write: commit input value to register RAM will start
emitting in next time unit
basic RAM design
width: width of their words eg. 32 or 64 bits
size: number of words eg. hundreds of millions

## Slide 42: RAM multi registers
Stack registers memory bank of any length
Random Access Memory
Directly access randomly chosen words irrespective of its physical location in equal speed
For n-register RAM
Stack n registers
Assign unique address (k = 0 – n-1)
Build gate logic to select register at address k
3 inputs: data input, address input, and load bit
load = 0 read: RAM outputs value of selected register
load = 1 write: commit input value to register RAM will start
emitting in next time unit
basic RAM design
width: width of their words eg. 32 or 64 bits
size: number of words eg. hundreds of millions

## Slide 43: RAM multi registers
Stack registers memory bank of any length
Random Access Memory
Directly access randomly chosen words irrespective of its physical location in equal speed
For n-register RAM
Stack n registers
Assign unique address (k = 0 – n-1)
Build gate logic to select register at address k
3 inputs: data input, address input, and load bit
load = 0 read: RAM outputs value of selected register
load = 1 write: commit input value to register RAM will start
emitting in next time unit
basic RAM design
width: width of their words eg. 32 or 64 bits
size: number of words eg. hundreds of millions

## Slide 44: RAM multi registers
Stack registers memory bank of any length
Random Access Memory
Directly access randomly chosen words irrespective of its physical location in equal speed
For n-register RAM
Stack n registers
Assign unique address (k = 0 – n-1)
Build gate logic to select register at address k
3 inputs: data input, address input, and load bit
load = 0 read: RAM outputs value of selected register
load = 1 write: commit input value to register RAM will start
emitting in next time unit
basic RAM design
width: width of their words eg. 32 or 64 bits
size: number of words eg. hundreds of millions

## Slide 45: RAM multi registers
Stack registers memory bank of any length
Random Access Memory
Directly access randomly chosen words irrespective of its physical location in equal speed
For n-register RAM
Stack n registers
Assign unique address (k = 0 – n-1)
Build gate logic to select register at address k
3 inputs: data input, address input, and load bit
load = 0 read: RAM outputs value of selected register
load = 1 write: commit input value to register RAM will start
emitting in next time unit
basic RAM design
width: width of their words eg. 32 or 64 bits
size: number of words eg. hundreds of millions

## Slide 46: RAM ram8
Using Ch1 and Ch 3 gates
Build combinational logic that, given a certain address value, takes the RAM8’s in input and loads it into the selected register
Line up an array of eight registers
Build combinational logic that, given a certain address value, selects the right register and pipes its out value to the RAM8’s out

## Slide 47
Using Ch1 and Ch 3 gates
Build combinational logic that, given a certain address value, takes the RAM8’s in input and loads it into the selected register
Line up an array of eight registers
Build combinational logic that, given a certain address value, selects the right register and pipes its out value to the RAM8’s out
RAM ram8

## Slide 48: RAM ram8
Using Ch1 and Ch 3 gates
Build combinational logic that, given a certain address value, takes the RAM8’s in input and loads it into the selected register
Line up an array of 8 registers
Build combinational logic that, given a certain address value, selects the right register and pipes its out value to the RAM8’s out

## Slide 49: RAM ram8
Using Ch1 and Ch 3 gates
Build combinational logic that, given a certain address value, takes the RAM8’s in input and loads it into the selected register
Line up an array of 8 registers
Build combinational logic that, given a certain address value, selects the right register and pipes its out value to the RAM8’s out

## Slide 50: RAM ram8
Using Ch1 and Ch 3 gates
Build combinational logic that, given a certain address value, takes the RAM8’s in input and loads it into the selected register
Line up an array of 8 registers
Build combinational logic that, given a certain address value, selects the right register and pipes its out value to the RAM8’s out
/**
* Memory of 8 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM8 {
IN in[16], load, address[3];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address, a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
Register(in=in, load=load0, out=o0);
Register(in=in, load=load1, out=o1);
Register(in=in, load=load2, out=o2);
Register(in=in, load=load3, out=o3);
Register(in=in, load=load4, out=o4);
Register(in=in, load=load5, out=o5);
Register(in=in, load=load6, out=o6);
Register(in=in, load=load7, out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address, out=out);
}

## Slide 51: RAM ram8
Using Ch1 and Ch 3 gates
Build combinational logic that, given a certain address value, takes the RAM8’s in input and loads it into the selected register
Line up an array of 8 registers
Build combinational logic that, given a certain address value, selects the right register and pipes its out value to the RAM8’s out
/**
* Memory of 8 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM8 {
IN in[16], load, address[3];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address, a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
Register(in=in, load=load0, out=o0);
Register(in=in, load=load1, out=o1);
Register(in=in, load=load2, out=o2);
Register(in=in, load=load3, out=o3);
Register(in=in, load=load4, out=o4);
Register(in=in, load=load5, out=o5);
Register(in=in, load=load6, out=o6);
Register(in=in, load=load7, out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address, out=out);
}

## Slide 52: RAM ram8
Using Ch1 and Ch 3 gates
Build combinational logic that, given a certain address value, takes the RAM8’s in input and loads it into the selected register
Line up an array of 8 registers
Build combinational logic that, given a certain address value, selects the right register and pipes its out value to the RAM8’s out
/**
* Memory of 8 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM8 {
IN in[16], load, address[3];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address, a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
Register(in=in, load=load0, out=o0);
Register(in=in, load=load1, out=o1);
Register(in=in, load=load2, out=o2);
Register(in=in, load=load3, out=o3);
Register(in=in, load=load4, out=o4);
Register(in=in, load=load5, out=o5);
Register(in=in, load=load6, out=o6);
Register(in=in, load=load7, out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address, out=out);
}

## Slide 53: RAM ram8
Using Ch1 and Ch 3 gates
Build combinational logic that, given a certain address value, takes the RAM8’s in input and loads it into the selected register
Line up an array of 8 registers
Build combinational logic that, given a certain address value, selects the right register and pipes its out value to the RAM8’s out
/**
* Memory of 8 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM8 {
IN in[16], load, address[3];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address, a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
Register(in=in, load=load0, out=o0);
Register(in=in, load=load1, out=o1);
Register(in=in, load=load2, out=o2);
Register(in=in, load=load3, out=o3);
Register(in=in, load=load4, out=o4);
Register(in=in, load=load5, out=o5);
Register(in=in, load=load6, out=o6);
Register(in=in, load=load7, out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address, out=out);
}

## Slide 54: RAM ram64
A memory bank of arbitrary length (a power of 2) is built recursively from smaller memory units (registers all the way down)
Eg. 64-register RAM can be built from an array of eight 8-register RAM chips
In RAM64, we use a 6-bit address xxxyyy
The MSB xxx bits select one of the RAM8 chips, and the LSB yyy bits select one of the registers within the selected RAM8.

## Slide 55: RAM ram64
A memory bank of arbitrary length (a power of 2) is built recursively from smaller memory units (registers all the way down)
Eg. 64-register RAM can be built from an array of eight 8-register RAM chips
In RAM64, we use a 6-bit address xxxyyy
The MSB xxx bits select one of the RAM8 chips, and the LSB yyy bits select one of the registers within the selected RAM8.

## Slide 56: RAM ram64
A memory bank of arbitrary length (a power of 2) is built recursively from smaller memory units (registers all the way down)
Eg. 64-register RAM can be built from an array of eight 8-register RAM chips
In RAM64, we use a 6-bit address xxxyyy
The MSB xxx bits select one of the RAM8 chips, and the LSB yyy bits select one of the registers within the selected RAM8.

## Slide 57: RAM ram64
A memory bank of arbitrary length (a power of 2) is built recursively from smaller memory units (registers all the way down)
Eg. 64-register RAM can be built from an array of eight 8-register RAM chips
In RAM64, we use a 6-bit address xxxyyy
The MSB xxx bits select one of the RAM8 chips, and the LSB yyy bits select one of the registers within the selected RAM8.

## Slide 58: RAM ram64
/**
* Memory of 64 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM64 {
IN in[16], load, address[6];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address[0..2], a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
RAM8(in=in, load=load0, address=address[3..5], out=o0);
RAM8(in=in, load=load1, address=address[3..5], out=o1);
RAM8(in=in, load=load2, address=address[3..5], out=o2);
RAM8(in=in, load=load3, address=address[3..5], out=o3);
RAM8(in=in, load=load4, address=address[3..5], out=o4);
RAM8(in=in, load=load5, address=address[3..5], out=o5);
RAM8(in=in, load=load6, address=address[3..5], out=o6);
RAM8(in=in, load=load7, address=address[3..5], out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address[0..2], out=out);
}
A memory bank of arbitrary length (a power of 2) is built recursively from smaller memory units (registers all the way down)
Eg. 64-register RAM can be built from an array of eight 8-register RAM chips
In RAM64, we use a 6-bit address xxxyyy
The MSB xxx bits select one of the RAM8 chips, and the LSB yyy bits select one of the registers within the selected RAM8.

## Slide 59: RAM ram64
/**
* Memory of 64 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM64 {
IN in[16], load, address[6];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address[0..2], a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
RAM8(in=in, load=load0, address=address[3..5], out=o0);
RAM8(in=in, load=load1, address=address[3..5], out=o1);
RAM8(in=in, load=load2, address=address[3..5], out=o2);
RAM8(in=in, load=load3, address=address[3..5], out=o3);
RAM8(in=in, load=load4, address=address[3..5], out=o4);
RAM8(in=in, load=load5, address=address[3..5], out=o5);
RAM8(in=in, load=load6, address=address[3..5], out=o6);
RAM8(in=in, load=load7, address=address[3..5], out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address[0..2], out=out);
}
A memory bank of arbitrary length (a power of 2) is built recursively from smaller memory units (registers all the way down)
Eg. 64-register RAM can be built from an array of eight 8-register RAM chips
In RAM64, we use a 6-bit address xxxyyy
The MSB xxx bits select one of the RAM8 chips, and the LSB yyy bits select one of the registers within the selected RAM8.

## Slide 60: RAM ram64
/**
* Memory of 64 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM64 {
IN in[16], load, address[6];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address[0..2], a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
RAM8(in=in, load=load0, address=address[3..5], out=o0);
RAM8(in=in, load=load1, address=address[3..5], out=o1);
RAM8(in=in, load=load2, address=address[3..5], out=o2);
RAM8(in=in, load=load3, address=address[3..5], out=o3);
RAM8(in=in, load=load4, address=address[3..5], out=o4);
RAM8(in=in, load=load5, address=address[3..5], out=o5);
RAM8(in=in, load=load6, address=address[3..5], out=o6);
RAM8(in=in, load=load7, address=address[3..5], out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address[0..2], out=out);
}
A memory bank of arbitrary length (a power of 2) is built recursively from smaller memory units (registers all the way down)
Eg. 64-register RAM can be built from an array of eight 8-register RAM chips
In RAM64, we use a 6-bit address xxxyyy
The MSB xxx bits select one of the RAM8 chips, and the LSB yyy bits select one of the registers within the selected RAM8.

## Slide 61: RAM ram64
/**
* Memory of 64 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM64 {
IN in[16], load, address[6];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address[0..2], a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
RAM8(in=in, load=load0, address=address[3..5], out=o0);
RAM8(in=in, load=load1, address=address[3..5], out=o1);
RAM8(in=in, load=load2, address=address[3..5], out=o2);
RAM8(in=in, load=load3, address=address[3..5], out=o3);
RAM8(in=in, load=load4, address=address[3..5], out=o4);
RAM8(in=in, load=load5, address=address[3..5], out=o5);
RAM8(in=in, load=load6, address=address[3..5], out=o6);
RAM8(in=in, load=load7, address=address[3..5], out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address[0..2], out=out);
}
A memory bank of arbitrary length (a power of 2) is built recursively from smaller memory units (registers all the way down)
Eg. 64-register RAM can be built from an array of eight 8-register RAM chips
In RAM64, we use a 6-bit address xxxyyy
The MSB xxx bits select one of the RAM8 chips, and the LSB yyy bits select one of the registers within the selected RAM8.

## Slide 62: RAM ram64
/**
* Memory of 64 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM64 {
IN in[16], load, address[6];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address[0..2], a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
RAM8(in=in, load=load0, address=address[3..5], out=o0);
RAM8(in=in, load=load1, address=address[3..5], out=o1);
RAM8(in=in, load=load2, address=address[3..5], out=o2);
RAM8(in=in, load=load3, address=address[3..5], out=o3);
RAM8(in=in, load=load4, address=address[3..5], out=o4);
RAM8(in=in, load=load5, address=address[3..5], out=o5);
RAM8(in=in, load=load6, address=address[3..5], out=o6);
RAM8(in=in, load=load7, address=address[3..5], out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address[0..2], out=out);
}
A memory bank of arbitrary length (a power of 2) is built recursively from smaller memory units (registers all the way down)
Eg. 64-register RAM can be built from an array of eight 8-register RAM chips
In RAM64, we use a 6-bit address xxxyyy
The MSB xxx bits select one of the RAM8 chips, and the LSB yyy bits select one of the registers within the selected RAM8.

## Slide 63: RAM ram512
/**
* Memory of 512 registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM512 {
IN in[16], load, address[9];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address[0..2], a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
RAM64(in=in, load=load0, address=address[3..8], out=o0);
RAM64(in=in, load=load1, address=address[3..8], out=o1);
RAM64(in=in, load=load2, address=address[3..8], out=o2);
RAM64(in=in, load=load3, address=address[3..8], out=o3);
RAM64(in=in, load=load4, address=address[3..8], out=o4);
RAM64(in=in, load=load5, address=address[3..8], out=o5);
RAM64(in=in, load=load6, address=address[3..8], out=o6);
RAM64(in=in, load=load7, address=address[3..8], out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address[0..2], out=out);
}
RAM512

## Slide 64: RAM ram4k
RAM4K
/**
* Memory of 4K registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM4K {
IN in[16], load, address[12];
OUT out[16];
PARTS:
DMux8Way(in=load, sel=address[0..2], a=load0, b=load1, c=load2, d=load3, e=load4, f=load5, g=load6, h=load7);
RAM512(in=in, load=load0, address=address[3..11], out=o0);
RAM512(in=in, load=load1, address=address[3..11], out=o1);
RAM512(in=in, load=load2, address=address[3..11], out=o2);
RAM512(in=in, load=load3, address=address[3..11], out=o3);
RAM512(in=in, load=load4, address=address[3..11], out=o4);
RAM512(in=in, load=load5, address=address[3..11], out=o5);
RAM512(in=in, load=load6, address=address[3..11], out=o6);
RAM512(in=in, load=load7, address=address[3..11], out=o7);
Mux8Way16(a=o0, b=o1, c=o2, d=o3, e=o4, f=o5, g=o6, h=o7, sel=address[0..2], out=out);
}

## Slide 65: RAM ram16k
RAM512
/**
* Memory of 16K registers, each 16 bit-wide. Out holds the value
* stored at the memory location specified by address. If load==1, then
* the in value is loaded into the memory location specified by address
* (the loaded value will be emitted to out from the next time step onward).
*/
CHIP RAM16K {
IN in[16], load, address[14];
OUT out[16];
PARTS:
DMux4Way(in=load, sel=address[0..1], a=load0, b=load1, c=load2, d=load3);
RAM4K(in=in, load=load0, address=address[2..13], out=o0);
RAM4K(in=in, load=load1, address=address[2..13], out=o1);
RAM4K(in=in, load=load2, address=address[2..13], out=o2);
RAM4K(in=in, load=load3, address=address[2..13], out=o3);
Mux4Way16(a=o0, b=o1, c=o2, d=o3, sel=address[0..1], out=out);
}

## Slide 66: Counter
A counter is a sequential chip whose state is an integer number that increments every time unit
where usually
A program counter outputs the address of the instruction in the current program
Usually, the counter has to increment itself by 1 in each clock cycle computer fetches the next instruction
Sometimes, ‘‘jump to execute instruction number n’’: set the counter to n continue counting with n+1, n+2, etc.
Reset the counter
Resetting to 0 restarts the program
Also, allow for decrementing instead of incrementing

## Slide 67: Counter
A counter is a sequential chip whose state is an integer number that increments every time unit
where usually
A program counter outputs the address of the instruction in the current program
Usually, the counter has to increment itself by 1 in each clock cycle computer fetches the next instruction
Sometimes, ‘‘jump to execute instruction number n’’: set the counter to n continue counting with n+1, n+2, etc.
Reset the counter
Resetting to 0 restarts the program
Also, allow for decrementing instead of incrementing

## Slide 68: Counter
A counter is a sequential chip whose state is an integer number that increments every time unit
where usually
A program counter outputs the address of the instruction in the current program
Usually, the counter has to increment itself by 1 in each clock cycle computer fetches the next instruction
Sometimes, ‘‘jump to execute instruction number n’’: set the counter to n continue counting with n+1, n+2, etc.
Reset the counter
Resetting to 0 restarts the program
Also, allow for decrementing instead of incrementing

## Slide 69: Counter
A counter is a sequential chip whose state is an integer number that increments every time unit
where usually
A program counter outputs the address of the instruction in the current program
Usually, the counter has to increment itself by 1 in each clock cycle computer fetches the next instruction
Sometimes, ‘‘jump to execute instruction number n’’: set the counter to n continue counting with n+1, n+2, etc.
Reset the counter
Resetting to 0 restarts the program
Also, allow for decrementing instead of incrementing

## Slide 70: Counter
A counter is a sequential chip whose state is an integer number that increments every time unit
where usually
A program counter outputs the address of the instruction in the current program
Usually, the counter has to increment itself by 1 in each clock cycle computer fetches the next instruction
Sometimes, ‘‘jump to execute instruction number n’’: set the counter to n continue counting with n+1, n+2, etc.
Reset the counter
Resetting to 0 restarts the program
Also, allow for decrementing instead of incrementing

## Slide 71: Counter
A counter is a sequential chip whose state is an integer number that increments every time unit
where usually
A program counter outputs the address of the instruction in the current program
Usually, the counter has to increment itself by 1 in each clock cycle computer fetches the next instruction
Sometimes, ‘‘jump to execute instruction number n’’: set the counter to n continue counting with n+1, n+2, etc.
Reset the counter
Resetting to 0 restarts the program
Also, allow for decrementing instead of incrementing

## Slide 72: Counter
A counter is a sequential chip whose state is an integer number that increments every time unit
where usually
A program counter outputs the address of the instruction in the current program
Usually, the counter has to increment itself by 1 in each clock cycle computer fetches the next instruction
Sometimes, ‘‘jump to execute instruction number n’’: set the counter to n continue counting with n+1, n+2, etc.
Reset the counter
Resetting to 0 restarts the program
Also, allow for decrementing instead of incrementing

## Slide 73: Counter
A counter is a sequential chip whose state is an integer number that increments every time unit
where usually
A program counter outputs the address of the instruction in the current program
Usually, the counter has to increment itself by 1 in each clock cycle computer fetches the next instruction
Sometimes, ‘‘jump to execute instruction number n’’: set the counter to n continue counting with n+1, n+2, etc.
Reset the counter
Resetting to 0 restarts the program
Also, allow for decrementing instead of incrementing

## Slide 74: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0

## Slide 75: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0

## Slide 76: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0

## Slide 77: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0

## Slide 78: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0

## Slide 79: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0

## Slide 80: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
Eg.
Time 22: in = 527 and out = 47
Time 23: reset = 1 Time 24: out = 0
  out = 0 until inc = 1
Time 25: inc = 1 Time 26: out = 1
  regular counting continues until load = 1
Time 29: load = 1 Time 30: out = in = 527
  since still inc = 1, regular incrementing until inc = 0

## Slide 81: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
Eg.
Time 22: in = 527 and out = 47
Time 23: reset = 1 Time 24: out = 0
  out = 0 until inc = 1
Time 25: inc = 1 Time 26: out = 1
  regular counting continues until load = 1
Time 29: load = 1 Time 30: out = in = 527
  since still inc = 1, regular incrementing until inc = 0

## Slide 82: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
Eg.
Time 22: in = 527 and out = 47
Time 23: reset = 1 Time 24: out = 0
  out = 0 until inc = 1
Time 25: inc = 1 Time 26: out = 1
  regular counting continues until load = 1
Time 29: load = 1 Time 30: out = in = 527
  since still inc = 1, regular incrementing until inc = 0

## Slide 83: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
Eg.
Time 22: in = 527 and out = 47
Time 23: reset = 1 Time 24: out = 0
  out = 0 until inc = 1
Time 25: inc = 1 Time 26: out = 1
  regular counting continues until load = 1
Time 29: load = 1 Time 30: out = in = 527
  since still inc = 1, regular incrementing until inc = 0

## Slide 84: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
Eg.
Time 22: in = 527 and out = 47
Time 23: reset = 1 Time 24: out = 0
  out = 0 until inc = 1
Time 25: inc = 1 Time 26: out = 1
  regular counting continues until load = 1
Time 29: load = 1 Time 30: out = in = 527
  since still inc = 1, regular incrementing until inc = 0

## Slide 85: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
Eg.
Time 22: in = 527 and out = 47
Time 23: reset = 1 Time 24: out = 0
  out = 0 until inc = 1
Time 25: inc = 1 Time 26: out = 1
  regular counting continues until load = 1
Time 29: load = 1 Time 30: out = in = 527
  since still inc = 1, regular incrementing until inc = 0

## Slide 86: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
Eg.
Time 22: in = 527 and out = 47
Time 23: reset = 1 Time 24: out = 0
  out = 0 until inc = 1
Time 25: inc = 1 Time 26: out = 1
  regular counting continues until load = 1
Time 29: load = 1 Time 30: out = in = 527
  since still inc = 1, regular incrementing until inc = 0

## Slide 87: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
Eg.
Time 22: in = 527 and out = 47
Time 23: reset = 1 Time 24: out = 0
  out = 0 until inc = 1
Time 25: inc = 1 Time 26: out = 1
  regular counting continues until load = 1
Time 29: load = 1 Time 30: out = in = 527
  since still inc = 1, regular incrementing until inc = 0

## Slide 88: Counter
A counter chip = input/output logic of a standard register + combinatorial logic for adding a constant
The combinational logic
Computes the counting function
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
Eg.
Time 22: in = 527 and out = 47
Time 23: reset = 1 Time 24: out = 0
  out = 0 until inc = 1
Time 25: inc = 1 Time 26: out = 1
  regular counting continues until load = 1
Time 29: load = 1 Time 30: out = in = 527
  since still inc = 1, regular incrementing until inc = 0

## Slide 89: Counter
Puts the counter in the right operating mode, according to its 3 control bits: inc, load, reset
    If inc = 1, the counter increments its state in every clock cycle
    If load = 1 and input = d, the counter is initialized to counting base d (most of this logic was built in Ch 2)
    If reset = 1, the counter resets to 0
/**
* A 16-bit counter with load and reset control bits.
* if (reset[t] == 1) out[t+1] = 0
* else if (load[t] == 1) out[t+1] = in[t]
* else if (inc[t] == 1) out[t+1] = out[t] + 1 (integer addition)
* else out[t+1] = out[t]
*/
CHIP PC {
IN in[16],load,inc,reset;
OUT out[16];
PARTS:
Inc16(in=o, out=oinc);
Mux4Way16(a=oinc, b=in, c=false, d=false,
sel[0]=load, sel[1]=reset, out=o1);
Or8Way(in[0]=load, in[1]=inc, in[2]=reset,
in[3..7]=false, out=or);
Register(in=o1, load=or, out=o, out=out);
}

## Slide 90: Perspective
In combinational chips (time neither modeled nor recognized) feedback loops are problematic
The output would depend on the input, which itself would depend on the output,
and thus the output would depend on itself
Sequential chips require feedback loops
Sequential chips = combinational + DFF sandwhich
DFFs have inherent time delay the output(t) does not depend on itself,
but rather on output(t-1) guarded against uncontrolled ‘‘data races’’
Their outputs change only during the transition between a clock cycle to the next,
and not within the cycle itself (in fact, they might be unstable states during clock cycles but we don’t care)

## Slide 91: Perspective
In combinational chips (time neither modeled nor recognized) feedback loops are problematic
The output would depend on the input, which itself would depend on the output,
and thus the output would depend on itself
Sequential chips require feedback loops
Sequential chips = combinational + DFF sandwhich
DFFs have inherent time delay the output(t) does not depend on itself,
but rather on output(t-1) guarded against uncontrolled ‘‘data races’’
Their outputs change only during the transition between a clock cycle to the next,
and not within the cycle itself (in fact, they might be unstable states during clock cycles but we don’t care)

## Slide 92: Perspective
In combinational chips (time neither modeled nor recognized) feedback loops are problematic
The output would depend on the input, which itself would depend on the output,
and thus the output would depend on itself
Sequential chips require feedback loops
Sequential chips = combinational + DFF sandwhich
DFFs have inherent time delay the output(t) does not depend on itself,
but rather on output(t-1) guarded against uncontrolled ‘‘data races’’
Their outputs change only during the transition between a clock cycle to the next,
and not within the cycle itself (in fact, they might be unstable states during clock cycles but we don’t care)

## Slide 93: Perspective
In combinational chips (time neither modeled nor recognized) feedback loops are problematic
The output would depend on the input, which itself would depend on the output,
and thus the output would depend on itself
Sequential chips require feedback loops
Sequential chips = combinational + DFF sandwhich
DFFs have inherent time delay the output(t) does not depend on itself,
but rather on output(t-1) guarded against uncontrolled ‘‘data races’’
Their outputs change only during the transition between a clock cycle to the next,
and not within the cycle itself (in fact, they might be unstable states during clock cycles but we don’t care)

## Slide 94: Perspective
In combinational chips (time neither modeled nor recognized) feedback loops are problematic
The output would depend on the input, which itself would depend on the output,
and thus the output would depend on itself
Sequential chips require feedback loops
Sequential chips = combinational + DFF sandwhich
DFFs have inherent time delay the output(t) does not depend on itself,
but rather on output(t-1) guarded against uncontrolled ‘‘data races’’
Their outputs change only during the transition between a clock cycle to the next,
and not within the cycle itself (in fact, they might be unstable states during clock cycles but we don’t care)

## Slide 95: Perspective
In combinational chips (time neither modeled nor recognized) feedback loops are problematic
The output would depend on the input, which itself would depend on the output,
and thus the output would depend on itself
Sequential chips require feedback loops
Sequential chips = combinational + DFF sandwhich
DFFs have inherent time delay the output(t) does not depend on itself,
but rather on output(t-1) guarded against uncontrolled ‘‘data races’’
Their outputs change only during the transition between a clock cycle to the next,
and not within the cycle itself (in fact, they might be unstable states during clock cycles but we don’t care)

## Slide 96: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips

## Slide 97: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips

## Slide 98: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
x is in nearby register
y is in a remote RAM register
ALU
x
y

## Slide 99: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
x is in nearby register
y is in a remote RAM register
ALU
x
y
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y | y
clock |  |  |  |  |  |  |  |  |  | 
y
x
input 2
input 1

## Slide 100: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
*#^( + %$@&
%$@&
*#^(
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y | y
clock |  |  |  |  |  |  |  |  |  | 
y
x

## Slide 101: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
*#^( + %$@&
%$@&
*#^(
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y | y
clock |  |  |  |  |  |  |  |  |  | 
y
x

## Slide 102: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
*#^( + %$@&
%$@&
*#^(
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y | y
clock |  |  |  |  |  |  |  |  |  | 
y
x

## Slide 103: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
*#^( + %$@&
%$@&
*#^(
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y | y
clock |  |  |  |  |  |  |  |  |  | 
signal from x arrives before y
x
y

## Slide 104: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
*#^( + %$@&
%$@&
x
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y | y
clock |  |  |  |  |  |  |  |  |  | 
signal from x arrives before y
x
y

## Slide 105: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
x + %$@&
%$@&
x
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y | y
clock |  |  |  |  |  |  |  |  |  | 
signal from x arrives before y
x
y

## Slide 106: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
x + %$@&
%$@&
x
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y | y
clock |  |  |  |  |  |  |  |  |  | 
signal from x arrives before y
y
x

## Slide 107: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
x + %$@&
%$@&
x
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y
clock |  |  |  |  |  |  |  |  |  | 
signal from x arrives before y
y
x

## Slide 108: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
x + %$@&
%$@&
x
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y
clock |  |  |  |  |  |  |  |  |  | 
signal from x arrives before y
y
x

## Slide 109: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
x + %$@&
y
x
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y
clock |  |  |  |  |  |  |  |  |  | 
signal from x arrives before y
x
y

## Slide 110: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
x + y
y
x
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y
clock |  |  |  |  |  |  |  |  |  | 
signal from x arrives before y
x
y

## Slide 111: Perspective
‘Discretization’ of the sequential chips’ outputs synchronizes the overall computer architecture
Eg. You tell the ALU to compute x+y
The length of the computer cycle has to be slightly longer than time it takes to travel the longest distance between two chips
physical constraints
(distance, resistance, interference, random noise, etc.)
x is in nearby register
y is in a remote RAM register
ALU constantly computes whatever inputs it sees
ALU computes x + garbage until y arrives
ALU
x
y
x + y
y
x
out | *#^( + %$@& | *#^( + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + %$@& | x + y | x + y
input 1 | *#^( | *#^( | x | x | x | x | x | x | x | X
input 2 | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | %$@& | y | y
clock |  |  |  |  |  |  |  |  |  | 
signal from x arrives before y
x
y